Control
block
ROM
ROM
ROM
IR
MDR
REG_SEL
RAM
REGS (16)
R0 - R15
SP
Flags
Zero padded, Low 4-bit
 ALU
A
MAR
ADRL
Z
ADRH
PC
F1 ц-architecture
Ver 1.3
ADRESS (8-bit)
DATA (4-bit)

---
F1 architecture overview
- Word size 4-bit
- Two internal buses
  - ADR for address; 8-bit wide
  - DTA for data; 4-bit wide
- Addresses are layed out big-endian style
- 4-bit OP codes, leading to 16 operations maximum
- Each instruction laid out in memory as
  - <op code> <opt1> <opt2>
- Only immediate address mode
- Each instruction is time capped to 6 clock ticks for ease of programming
- A 16-word stack exists as target for push and pop ops and to allow for function calls
- 16 general purpose registers (R0-R15)
- A 4 bit OUT register for display purposes

---
ISA
Mnemonic	Ц pseudo code	Enc.	Flags			Example
			C	Z	V
ld $IMM8, <REG>	RAM[IMM8] → <REG>	0 H L <REG>				ld $1A, R1
st <REG>, $IMM8	<REG> → RAM[IMM8]	1 <REG> H L				st R2, $1A
mv <REG1>, <REG2>	<REG1> → <REG2>	2 <REG1> <REG2>				mv R2, R1
mv #IMM4, <REG>	IMM4 → <REG>	3 IMM4 <REG>				mv #3, R1
sub <REG1>, <REG2>	<REG1> - <REG2> → <REG2>	4 <REG1> <REG2>		x		sub R1, R2
add <REG1>, <REG2>	<REG1> + <REG2> → <REG2>	5 <REG1> <REG2>	x	x	x	add R1, R2
or <REG1>, <REG2>	<REG1> OR <REG2> → <REG2>	6 <REG1> <REG2>		x		or R1, R2
not <REG>	NOT <REG> → <REG>	7 <REG>		x		not R1
brz $IMM8	IF Z == 1: IMM8 → PC	8 H L				brz $12
brc $IMM8	IF C == 1: IMM8 → PC	9 H L				brc $12
jmp $IMM8	IMM8 → PC	A H L				jmp $12
rol <REG>	<REG> << 1 → <REG>	B <REG>	x	x		rol R1, R2
push <REG>	<REG> → ST[SP]; SP++	C <REG>				push R1
pop <REG>	ST[SP] → <REG>; SP--	D <REG>				pop R1
call $IMM8	PUSH PC_HI / PUSH PC_LO / IMM8 → PC	E H L				call $12
ret	POP PC_LO / POP PC_HI	F				ret